## Slide 1: Software Safety Basics
(Herrmann, Ch. 2)

## Slide 2: Patriot missile defense system failure
On February 25, 1991, a Patriot missile defense system operating at Dhahran, Saudi Arabia, during Operation Desert Storm failed to track and intercept an incoming Scud. This Scud subsequently hit an Army barracks, killing 28 Americans. [GAO]
http://news.bbc.co.uk/1/shared/spl/hi/middle_east/03/v3_iraq_timeline/html/scuds.stm

## Slide 3: Patriot: A software failure
[A] software problem in the system’s weapons control computer… led to an inaccurate tracking calculation that became worse the longer the system operated.
At the time of the incident, the battery had been operating continuously for over 100 hours. By then, the inaccuracy was serious enough to cause the system to look in the wrong place for the incoming Scud. [GAO]

## Slide 4: Tracking a missile: what should happen
Search: Wide range scanned
When missile detected,
range gate calculates the next area to scan
Validation, Tracking: Only range gated area scanned

## Slide 5: Software design flaw
Range gate calculates predicated position from
  Time of last radar detection:
  integer, measuring tenths of seconds
  Known velocity of missile: floating-point value
Problem:
  Range gate used 24-bit registers, and each 0.1-second time increment added a little error
  Over time, this error became significant enough to cause range gate to miscalculate missile position

## Slide 6: What actually happened
Range gated area shifted, no longer accurate

## Slide 7: Sources of the problem
Patriot designed for use against slower (Mach 2) missiles, not Scuds (Mach 5)
  Proper calibration not performed – largely due to fear that adding an external recorder could crash the system(!)
Patriot system typically used in short intervals – no longer than 8 hours
  Supposed to be mobile, quick on/off, to avoid detection

## Slide 8: Ariane 5 failure
On 4 June 1996, the maiden flight of the Ariane 5 launcher ended in a failure. Only about 40 seconds after initiation of the flight sequence, at an altitude of about 3700m, the launcher veered off its flight path, broke up and exploded.
http://www.vuw.ac.nz/staff/stephen_marshall/SE/Failures/SE_Ariane.html

## Slide 9: Ariane 5: A software failure
Unexpectedly large values encountered during alignment of “inertial platform”
Attempt to convert overly large 64-bit value into a 16-bit value
Software exception
Guidance system (hardware) shutdown

## Slide 10: Sources of the problem
Alignment code reused from
(smaller, less powerful) Ariane 4
  Velocity values of Ariane 5 were out of range of Ariane 4
Ironically, alignment not even needed after lift-off!
Why was alignment code running?
  Engineers decided to leave it running for 40 seconds after planned lift-off time –
  Permitting easy restart if launch was put on hold briefly

## Slide 11: Panama Cancer Institute accidents (Gage & McCormick, 2004)
November 2000: 27 cancer patients given massive doses of radiation
  Partly due to flaws in Multidata software
  Medical physicists who used the software were found guilty of 2nd degree murder in Panama
  Note: In the well-known “Therac-25” incidents of the 1980s, software failures led to massive doses of radiation being administered to patients. Do we ever learn?...

## Slide 12: Multidata software
Used to plan radiation treatment
  Operator enters patient data
  Operator indicates placement of “blocks” (metal shields used to protect sensitive areas) through graphical editor
  Software provides 3D prediction of where radiation would be distributed
  From this data, dosage is determined

## Slide 13: Block placement editor
Blocks drawn as separate polygons
(There are 2 blocks in this picture)
Software limitation: At most 4 blocks
What if doctors want to use more blocks?
NRC Information Notice 2001-08, Supp. 2

## Slide 14: A “solution”
Note: This is a single unbroken line…
Software treated it as a single block
Now you can draw more blocks!
NRC Information Notice 2001-08, Supp. 2

## Slide 15: Fatal problem
Dosage prediction algorithm expected blocks in the form of polygons, but graphical editor allowed non-polygons
When run on non-polygon blocks, predictions were drastically wrong; overly high dosages prescribed

## Slide 16: What is software safety?
Features and procedures which ensure that
  a product performs predictably under normal and abnormal conditions, and
  the likelihood of an unplanned event occurring is minimized and its consequences controlled and contained;
thereby preventing accidental injury or death, whether intentional or unintentional. (Herrmann)

## Slide 17: Features and procedures
Features: built into the software itself
  Range checks; monitors; warnings/alarms
Procedures: concern the proper environment for the software, and its proper use
  Computer hardware that the software runs on
  Physical, mechanical components of environment
  Human users

## Slide 18: Normal and abnormal conditions
Abnormal conditions:
  Failure of hardware components
  Power outage
  Extreme environmental conditions (temperature, velocity)
What to do?
  Not necessarily the best reaction, but one that has the best chance of preventing injury or death
  Fail-safe: shut down
  Fail-operational: continue in “simpler” degraded mode

## Slide 19: Avoiding “unplanned events”
To Herrmann, human users are the primary source of such events
  Can produce unusual inputs or combinations of inputs
User interface design, testing can be crucial to software safety
  Understand user behavior
  Create interfaces that guide users toward “good” input

## Slide 20: Terminology alert #1
There are many definitions of “safety”…
Herrmann thinks of safety as a set of features and procedures
  Something you can actually see in the software
Leveson: “freedom from accidents or losses”
  This is an idealized property of the software – something to aim for rather than actually achieve
Storey distinguishes “safety” from “adequate safety”
  Here, “safety” is close to Leveson’s definition;
  “adequate safety” is closer to Herrman’s definition

## Slide 21: Fault, error and failure
Fault: cause of error
- Misinterpreted software requirements
- Code defects: code doesn’t implement required behavior
Error: dangerous state,
from which failure is possible
Failure: unacceptable system behavior

## Slide 22: Fault, error and failure: Example
Fault: memory device fails
- Note: failure of component means fault at higher level
- If memory device not used, fault remains hidden
Error: attempt at memory access is unsuccessful
- Now, presence of fault is evident
- But, software may be able to handle it “gracefully”
Failure: unsuccessful memory access results in computing an “out of bounds” value

## Slide 23: Faults: Hardware vs. software
Some hardware faults may be random
  Due to manufacturing defects or simple “wear and tear”
  Probability can be estimated statistically
  Well-known techniques to minimize random faults:
  error-correcting codes, redundant systems
Software faults are always systematic – not random
  Generated during design or specification – not execution
  Software is not manufactured and doesn’t “wear out”
  Techniques for minimizing random faults don’t work with systematic faults
    Ariane 5 had redundant systems – all running the same software!

## Slide 24: Fault management options
Avoidance: Prevent faults from entering the system during the design phase
  “good practices” in design – e.g. programming standards
Removal: Find faults in the system before release
  Testing – costly and not always very effective

## Slide 25: Fault management options
Tolerance: Find faults in operational system after release, allow system to proceed correctly
  Recovery blocks:
    Create duplicate code modules
    Run “primary module”, then run an “acceptance test”
    If test fails, roll back changes and run an “alternative module”
  N-version programming:
    several independent implementations of a program
    Goal: ensure “design diversity”, avoid common faults
  Both approaches are costly, and may not be very effective
    For a study on whether N-version programming really achieves “design diversity”, read Knight & Leveson’s article.

## Slide 26: Model of system failure behavior
Perfect
OK
Erroneous
error detected
error not detected
Fail
Operational
Fail Safe
Innocuous
Failure
Dangerous
Failure
Known Safe
State
Unknown or
Dangerous State
fault not introduced
fault introduced
fault
removed

## Slide 27: Terminology alert #2
“fault” and “error” have many alternative definitions
  Sometimes, “error” is a synonym for what we’re calling “fault”, and “fault” means “behavior that may trigger a failure”
  Following these alternative definitions, we have:
  error → fault → failure

## Slide 28: References
United States General Accounting Office. Report IMTEC-92-26, February 4, 1992. http://www.fas.org/spp/starwars/gao/im92026.htm
Ariane 5 Flight 501 Failure – Report by the Inquiry Board. July 19, 1996. http://sunnyday.mit.edu/accidents/Ariane5accidentreport.html
U.S. Nuclear Regulatory Commission. Update on radiation therapy overexposures in Panama. NRC Information Notice 2001-08, Supp. 2, November 20, 2001. http://www.hsrd.ornl.gov/nrc/special/IN200108s2.pdf
D. Gage and J. McCormick. Why software quality matters. Baseline, March 2004, 33-56. http://www.baselinemag.com/print_article2/0,1217,a=120920,00.asp
Nancy G. Leveson. Safeware: System Safety and Computers. Addison Wesley, 1995.
Neil Storey. Safety-Critical Computer Systems. Prentice Hall, 1996.
J.C. Knight and N.G. Leveson. An experimental evaluation of the assumption of independence in multiversion programming. IEEE Transactions on Software Engineering 12(1), 1986, 96-109.